## Slide 1: Advanced Reliability Analysis and RAVEN
RAVEN Workshop
PSA 2015 - April 26th 2015, Sun Valley (ID)

## Slide 2: Outline
Advanced Reliability Analysis: brief introduction
  Goal Oriented Sampling
  Concept of Limit Surface
  Convergence acceleration through ROMs
Reliability Analysis and RAVEN
  Available Goal Oriented Samplers
  Performing Reliability Analysis within RAVEN: workflow
Application examples of Reliability Analysis
RAVEN examples

## Slide 3: Reliability Analysis: INTRODUCTION

## Slide 4: Reliability Analysis: a quick introduction
Reliability theory evaluates the failure probability of a system given an interval of time
Failure is an “event”
  Goal is to forecast/assess the failure events of a given population or the event failure probability
Main goal
Compute the failure probability

## Slide 5: Reliability Analysis: Goal-oriented sampling
The evaluation of the failure probability might be computationally challenging, if traditional once-through sampling is employed:
  Rare events (low probability) require an enormous number of input space explorations:
    Computing a failure probability of 10-6 would require millions of Monte Carlo samples
  The information entropy contained in the already-evaluated histories is not used to adapt the sampling strategy:
    System response depends on many variables but often few are really important
    Adaptive Sampling based on Reliability (Limit) Surface search

## Slide 6: Reliability Analysis: Limit Surface Concept
Consider
System characterization
The limit surface can be described as the hyper-surface that classifies the input space with respect transition regions:
  The locus of points that divides the input domain with respect a boolean response (e.g. failure/success)
The goal function is an object that is defined as a part of the system outcome space. In a safety context, the goal function usually represents the success or failure (transition) of the system.

## Slide 7: Reliability Analysis: Limit Surface Concept (cont.)
If the system evolution is represented by
It is possible to identify the set of pairs
Let’s consider as the transition surface in the output space with respect to the goal function
Initial Conditions
Stochastic Parameters
in the input space, which leads the system outcome to match:

## Slide 8
Training on initial small number of sampled points
A fine grid is classified (failure or success) based on an user-specified surrogate model (sampling of the surrogate)
The limit surface is identified by the location of transition between failure/success
The furthest point on the limit surface from any other already tested point is chosen to test the classifier (convergence test)
Process iterates (24) until the limit surface converges
Limit surface
Failure
Success
Next point
Reliability Analysis: Limit Surface Search

## Slide 9: Reliability Analysis: ROMs
For the Adaptive Sampling based on the Reliability (Limit) Surface search, special types of ROMs called “classifiers” are used:
  A model (set of equations) that identifies to which category an object belongs in the feature (input) space
In RAVEN, these ROMs are used as acceleration schemes for goal oriented sampling strategies  they can be used to predict the location of the reliability (limit) surface
Let’s consider again a set of N data points
Based on the goal function :
Build a surrogate model of type “classifier”
  Reduced Order Model
Boolean vector

## Slide 10: Reliability Analysis and RAVEN

## Slide 11: Reliability Analysis and RAVEN: Samplers
RAVEN currently has 2 ways to perform Reliability Analysis based on Limit Surface Search:
Adaptive Sampler
Adaptive DET Sampler
All Coupled Codes
RELAP-7 only
Available
Available

## Slide 12
Define the distributions. Distributions are used to:
  Weigh the error estimation
  Generate a probability-weighted metric for grid construction
  Determine the probability of being inside one of the regions identified by the limit surface
Define the surrogate model to be used as the accelerator (of type Boolean or discrete)
Define the adaptive sampler:
  Convergence control and grid
  Import the acceleration ROM
  Associate the distribution with the variables
Define a step
Post-process the data to compute the failure probability
Reliability Analysis: Limit Surface Workflow

## Slide 13: Reliability Analysis: Applications

## Slide 14
Reliability Analysis: Applications
Fuel Performance - BISON
Smeared pellet stack with hafnium insulator end pellets:
  10 fuel pellets as a single, long pellet sandwiched between two insulator pellets.
10,000 second ramp from zero power to 25KW/m.
After the ramp the power was held constant to the end time of 1e8 seconds.
Notes: Mesh:
The BISON mesh that was used was a smeared pellet stack with hafnium insulator end pellets. This stack simulated 10 fuel pellets as a single, long pellet sandwiched between two insulator pellets. The insulator pellets each consisted of 4 axial elements and 11 radial elements for a total of 44 elements. The fuel consisted of 80 axial element and 11 radial elements for a total of 880 elements. Lastly, the cladding consisted of 135 axial elements and 5 radial elements for a total of 670 elements. The complete mesh and a zoomed in view can be seen in Figure 1A and 1B, respectively.

## Slide 15
Reliability Analysis: Applications
Pressurized Water Reactor Station Black Out
PWR SBO
100% Power
120% Power

## Slide 16
Reliability Analysis: Applications
Boiling Water Reactor Station Black Out
100% Power
120% Power
Notes: Scenario: LOOP + loss of DGs
3 recovery strategies: off-site power recovery, DG recovery, FW recovery
After loss of DGs, cooling is provided by RCIC/HPCI (mid figure); pressure control provided by SRV (left figure).
Torus pool temperature increases at each SRV activation (right figure).
When pool TH limits are reached, the RPV is depressurized; no cooling can be provided other than FW if available

## Slide 17: RAVEN Examples

## Slide 18: Workflow
Sample a model and create a database
Use generated data to seed the Adaptive Sampling Step
Compute failure probability from converged Solution
Train a ROM and compute the failure probability changing the stochastic parameters

## Slide 19: Exercise 1: Create a data set to seed the Adaptive Sampler

## Slide 20: 1 – Sample a Model to seed the Adaptive Sampler
Samplers
Models
Distributions
Steps
Databases
DataObjects
<Distributions>
<Normal name='normal_trunc'>
<mean>0.5</mean>
<sigma>0.1</sigma>
<lowerBound>0.0</lowerBound>
<upperBound>1.0</upperBound>
</Normal>
<Normal name='normal'>
<mean>2.0</mean>
<sigma>0.2</sigma>
</Normal>
<Uniform name='uniform'>
<upperBound>4.0</upperBound>
<lowerBound>1.0</lowerBound>
</Uniform>
</Distributions>
Truncation parameters
Input file name: 1-sample_Grid_seed_adaptive.xml

## Slide 21: 1 – Sample a Model to seed the Adaptive Sampler
Models
Distributions
<Models>
<ExternalModel name='PythonModule' subType=’’ ModuleToLoad='workshop_model’>
<variable>x1</variable>
<variable>x2</variable>
<variable>x3</variable>
<variable>y1</variable>
<variable>y2</variable>
<variable>y3</variable>
<variable>y4</variable>
<variable>y5</variable>
<variable>failure</variable>
</ExternalModel>
</Models>
Samplers
Steps
Databases
DataObjects
Input variables
Output variables
File name: workshop_model.py
Input file name: 1-sample_Grid_seed_adaptive.xml
Boolean Variable

## Slide 22: 1 – Sample a Model to seed the Adaptive Sampler
Samplers
Distributions
<Samplers>
<Grid name='Grid_function'>
<variable name='x1' >
<distribution>normal_trunc</distribution>
<grid type='value' lowerBound='0.0' construction='equal' steps='5'>0.2</grid>
</variable>
<variable name='x2' >
<distribution>normal</distribution>
<grid type='value' lowerBound='1.5' construction='equal' steps='5'>0.2</grid>
</variable>
<variable name='x3' >
<distribution>uniform</distribution>
<grid type='value' lowerBound='1.0' construction='equal' steps='5'>0.6</grid>
</variable>
</Grid>
</Samplers>
Models
Steps
Databases
DataObjects
<variable name>
<distribution>
<grid points>
Input file name: 1-sample_Grid_seed_adaptive.xml

## Slide 23: 1 – Sample a Model to seed the Adaptive Sampler
Distributions
<Databases>
<HDF5 name='out_db'/>
</Databases>
<DataObjects>
<TimePointSet name='inputPlaceHolder'>
<Input>x1,x2,x3</Input>
<Output>OutputPlaceHolder</Output>
</TimePointSet>
<TimePointSet name=’outGRID'>
<Input>x1,x2,x3</Input>
<Output>y1,y2,y3,y4,y5,failure</Output>
</TimePointSet>
</DataObjects>
Databases
DataObjects
Samplers
Models
Steps
<DataObjects>
<Inputs>
<Output>
Input file name: 1-sample_Grid_seed_adaptive.xml

## Slide 24: 1 – Sample a Model to seed the Adaptive Sampler
Distributions
Steps
Samplers
Models
Databases
DataObjects
Step
Model file
Model info
Sampler
Database
DataObjects
<Steps>
<MultiRun name='FirstMRun'>
<Input class='DataObjects' type='TimePoint' >inputPlaceHolder</Input>
<Model class='Models' type='ExternalModel’>PythonModule</Model>
<Sampler class='Samplers' type='Grid' >Grid_function</Sampler>
<Output class='DataObjects’ type='TimePointSet’ >outGRID</Output>
<Output class='Databases' type='HDF5' >out_db</Output>
<Output class='OutStreamManager' type='Print' >out_dump</Output>
<Output class='OutStreamManager' type='Plot' >plotResponse_y3</Output>
<Output class='OutStreamManager' type='Plot' >plotResponse_y4</Output>
<Output class='OutStreamManager' type='Plot' >plotResponse_y5</Output>
</MultiRun>
</Steps>
Input file name: 1-sample_Grid_seed_adaptive.xml

## Slide 25: Exercise 2: Use generated data to seed the Adaptive Sampling Step and perform Limit Surface search

## Slide 26: 2- Use data to seed the Adaptive Sampling Step
<Models>
<ExternalModel name='PythonModule' subType=’’
ModuleToLoad='workshop_model’>
<variable>x1</variable>
<variable>x2</variable>
<variable>x3</variable>
<variable>y2</variable>
<variable>y3</variable>
<variable>y4</variable>
<variable>y5</variable>
<variable>failure</variable>
</ExternalModel>
<ROM name=’AccelerationROM' subType='SciKitLearn'>
<Features>x1,x2,x3</Features>
<Target>goalFunction</Target>
<SKLtype>svm|SVC</SKLtype>
<kernel>rbf</kernel>
<C>10.0</C>
</ROM>
</Models>
Steps
Models
Steps
Databases
DataObjects
Functions
Samplers
Kernel Type
Penalty parameter of the error term
Input file name: 2-seeded_adaptive_sampling.xml
def run(self,Input): …
if self.y4 < 5.0:
self.failure= 0.0
else:
self.failure= 1.0
Transition definition:
0.0 -> success
1.0 -> failure

## Slide 27: 2- Use data to seed a Goal Oriented Sampling
<Functions>
<External name=’goalFunction’ file= ‘goalFunctionWorkshop’>
<variable>y4</variable>
<variable>failure</variable>
</External>
</Functions>
Models
Steps
Databases
DataObjects
Functions
Samplers
def __residuumSign(self): if self.y4 < 5.0: return 1
else : return -1
Variables that are needed for the evaluation
Transition definition:
1 -> success
-1 -> failure
Input file name: 2-seeded_adaptive_sampling.xml

## Slide 28: 2- Use data to seed the Adaptive Sampling Step
<Samplers>
<Adaptive name=’workshopAdaptive’>
<ROM class='Models' type='ROM’>accelerated_ROM</ROM>
<Function class='Functions' type='External’>goalFunction</Function>
<TargetEvaluation class='DataObjects' type='TimePointSet'>
outAdaptive
</TargetEvaluation>
<Convergence
limit='3000'
forceIteration='False'
weight='value'
persistence='25'>
1e-4
</Convergence>
<variable name='x1'><distribution>normal_trunc</distribution></variable>
<variable name='x2'><distribution>normal</distribution></variable>
<variable name='x3'><distribution>uniform</distribution></variable>
</Adaptive>
</Samplers>
Models
Steps
Databases
DataObjects
Functions
Samplers
Goal function
Max Iterations
Force Iteration until limit
Error Weighting: CDF or Value
Tolerance
Input file name: 2-seeded_adaptive_sampling.xml

## Slide 29: 2- Use data to seed a Goal Oriented Sampling
<Databases>
<HDF5 name='out_db_adaptive' directory=’DataBaseStorage/'/>
<HDF5 name='out_db’ filename='out_db.h5’ />
<HDF5 name='out_db_ls’ directory='DataBaseStorage/'/>
</Databases>
<DataObjects>
<TimePointSet name='outAdaptive'>
<Input>x1,x2,x3</Input>
<Output>y3,y4,y5,failure</Output>
</TimePointSet>
<TimePointSet name=’limitSurface'>
<Input>x1,x2,x3</Input>
<Output>goalFunction</Output>
</TimePointSet>
<TimePointSet name=’inputPlaceHolder'>
<Input>x1,x2,x3</Input>
<Output>OutputPlaceHolder</Output>
</TimePointSet>
</DataObjects>
Models
Steps
Databases
DataObjects
Functions
Samplers
Limit Surface Container
Input file name: 2-seeded_adaptive_sampling.xml

## Slide 30: 2- Use data to seed a Goal Oriented Sampling
<Steps>
<IOStep name=’load_seed_dataset'>
<Input class='Databases' type='HDF5' >out_db</Input>
<Output class='DataObjects’ type='TimePointSet'>outAdaptive</Output>
</IOStep>
<MultiRun name=’GoalOrientedStep'>
<Input class=DataObjects’ type=’TimePoint' >inputPlaceHolder</Input>
<Model class='Models' type='ExternalModel’>PythonModule</Model>
<Sampler class='Samplers' type=’Adaptive' >workshopAdaptive</Sampler>
<Output class='DataObjects’type='TimePointSet’ >outAdaptive</Output>
<Output class='Databases' type='HDF5' >out_db_adaptive</Output>
<SolutionExport class='DataObjects’type='TimePointSet’>
limitSurface
</SolutionExport >
</MultiRun>
<IOStep name=’push_limitsurface_in_database'>
<Input class='DataObjects' type='TimePointSet’ >limitSurface</Input>
<Output class='Databases' type='HDF5' >out_db_ls</Output>
</IOStep>
</Steps>>
Models
Steps
Databases
DataObjects
Functions
Samplers
Input file name: 2-seeded_adaptive_sampling.xml

## Slide 31: Exercise 3: Compute failure probability from Converged solution

## Slide 32: 3 –Failure Probability from Converged Solution
Models
<Models>
<ROM name=’probabilityROm' subType='SciKitLearn'>
<Features>x1,x2,x3</Features>
<Target>failure</Target>
<SKLtype>svm|SVC</SKLtype>
<C>10.0</C>
<kernel>rbf</kernel>
</ROM>
<ExternalModel name='PythonModule' subType=’’
ModuleToLoad='workshop_model’>
…
</ExternalModel>
<PostProcessor name=’computePb' subType=’BasicStatistics'>
<what>expectedValue</what>
<parameters>failure</paramters>
</PostProcessor>
</Models>
Samplers
Steps
Databases
DataObjects
Input file name: 3-compute_failure_pb_from_ls.xml

## Slide 33: 3 –Failure Probability from Converged Solution
Samplers
<Samplers>
<MonteCarlo name=’Montecarlo_sampling'>
<sampler_init> <limit>17576</limit> </sampler_init>
<variable name='x1’>
<distribution>normal_trunc</distribution>
</variable>
<variable name='x2’>
<distribution>normal</distribution>
</variable>
<variable name='x3’>
<distribution>uniform</distribution>
</variable>
</MonteCarlo>
</Samplers>
Model
Steps
Databases
DataObjects
Input file name: 3-compute_failure_pb_from_ls.xml

## Slide 34: 3 –Failure Probability from Converged Solution
<Databases>
<HDF5 name="out_ROM3_db"/>
<HDF5 name="out_db_montecarlo” directory=“DatabaseStorage/"/>
<HDF5 name="out_db_adaptive" filename="out_db_adaptive.h5” directory=“DatabaseStorage/"/>
</Databases>
<DataObjects>
<TimePointSet name=’outAdapt_failure'>
<Input>x1,x2,x3</Input>
<Output>failure</Output>
</TimePointSet>
<TimePointSet name=’outGrid_failure'>
<Input>x1,x2,x3</Input>
<Output>failure</Output>
</TimePointSet>
<TimePointSet name=’outMC_failure'>
<Input>x1,x2,x3</Input>
<Output>failure</Output>
</TimePointSet>
</DaDataObjectstas>
Databases
DataObjects
Samplers
Model
Steps
Input file name: 3-compute_failure_pb_from_ls.xml

## Slide 35: Exercise 4: Compute failure probability from Converged solution changing Distributions

## Slide 36: 4 – Compute failure probability changing distributions
Distributions
<Distributions>
<Normal name='normal_trunc'>
<mean>0.5</mean>
<sigma>0.1</sigma>
<lowerBound>0.0</lowerBound>
<upperBound>1.0</upperBound>
</Normal>
<Normal name='normal'>
<mean>2.0</mean>
<sigma>0.2</sigma>
</Normal>
<Uniform name='uniform'>
<upperBound>4.0</upperBound>
<lowerBound>1.0</lowerBound>
</Uniform>
</Distributions>
<Distributions>
<Normal name='normal_trunc'>
<mean>0.5</mean>
<sigma>0.2</sigma>
<lowerBound>0.0</lowerBound>
<upperBound>1.0</upperBound>
</Normal>
<Normal name='normal'>
<mean>1.5</mean>
<sigma>0.2</sigma>
</Normal>
<Uniform name='uniform'>
<upperBound>4.0</upperBound>
<lowerBound>1.5</lowerBound>
</Uniform>
</Distributions>
Input file name: 4-compute_pb_with_rom_and_changed_dists.xml

## Slide 37: Thank you Questions?