## Slide 1: Reliability Analysis on a BWR SBO Scenario Using RAVEN
RAVEN Workshop
Presenter: Andrea Alfonsi
IRUG 2016

## Slide 2: Outline
Advanced Reliability Analysis
  Goal Oriented Sampling
  Concept of Limit Surface
  Convergence acceleration through ROMs
Reliability Analysis and RAVEN
  Available Goal Oriented Samplers
  Performing Reliability Analysis within RAVEN: workflow
RAVEN application of Reliability Analysis on a BWR SBO scenario

## Slide 3: Reliability Analysis: INTRODUCTION

## Slide 4: Reliability Analysis: a quick introduction
Reliability theory evaluates the failure probability of a system given an interval of time
Failure is an “event”
  Goal is to forecast/assess the failure events of a given population or the event failure probability
Main goal
Compute the failure probability

## Slide 5: Reliability Analysis: Goal-oriented sampling
The evaluation of the failure probability might be computationally challenging, if traditional once-through sampling is employed:
  Rare events (low probability) require an enormous number of input space explorations:
    Computing a failure probability of 10-6 would require millions of Monte Carlo samples
  Information contained in the evaluated histories is not used to inform the sampling strategy:
    System response depends on many variables but often few are really important
    Adaptive Sampling based on Reliability (Limit) Surface search

## Slide 6: Reliability Analysis: Limit Surface Concept
System Response:
The limit surface can be described as the hyper-surface that classifies the input space with respect transition regions:
  The locus of points that divides the input domain with respect a boolean response (e.g. failure/success)
The goal function is an object that is defined as a part of the system outcome space. In a safety context, the goal function usually represents the success or failure (transition) of the system.

## Slide 7: Reliability Analysis: Limit Surface Concept
If the system evolution is represented by
It is possible to identify the set of pairs
Let’s consider as the transition surface in the output space with respect to the goal function
Initial Conditions
Stochastic Parameters
in the input space, which leads the system outcome to match:

## Slide 8
Training on initial small number of sampled points
A fine grid is classified (failure or success) based on an user-specified surrogate model (sampling of the surrogate)
The limit surface is identified by the location of transition between failure/success
The furthest point on the limit surface from any other already tested point is chosen to test the classifier (convergence test)
Process iterates (24) until the limit surface converges
Limit surface
Failure
Success
Next point
Reliability Analysis: Limit Surface Search

## Slide 9: Reliability Analysis: ROMs
For the Adaptive Sampling based on the Reliability (Limit) Surface search, special types of ROMs called “classifiers” are used:
  A model (set of equations) that identifies to which category an object belongs in the feature (input) space
In RAVEN, these ROMs are used as acceleration schemes for goal oriented sampling strategies  they can be used to predict the location of the reliability (limit) surface
Let’s consider again a set of N data points
Based on the goal function :
Build a surrogate model of type “classifier”
  Reduced Order Model
Boolean vector

## Slide 10: Reliability Analysis and RAVEN

## Slide 11: Reliability Analysis and RAVEN: Samplers
RAVEN has 2 ways to perform Reliability Analysis based on Limit Surface Search:
Adaptive Sampler
Adaptive DET Sampler
All Coupled Codes
RELAP5-3D, MAAP5 and RELAP7 only
Available
Available

## Slide 12
Define the distributions. Distributions are used to:
  Weigh the error estimation
  Generate a probability-weighted metric for grid construction
  Determine the probability of being inside one of the regions identified by the limit surface
Define the surrogate model to be used as the accelerator (of type Boolean or discrete)
Define the adaptive sampler:
  Convergence control and grid
  Import the acceleration ROM
  Associate the distribution with the variables
Define a step
Post-process the data to compute the failure probability
Reliability Analysis: Limit Surface Workflow

## Slide 13: Reliability Analysis on a BWR SBO scenario

## Slide 14: BWR SBO Scenario: Overview
Plant considered: BWR with Mk.I containment
Test case: Loss of Offsite Power (LOOP) + Loss of Diesel Generators
Objectives:
  Evaluate impact of power uprate on LOOP+SBO accident scenario
  Show capabilities of simulation based Probabilistic Risk Assessment (PRA) through RISMC

## Slide 15
BWR SBO Scenario: Key results
100% Power
120% Power
Notes: Scenario: LOOP + loss of DGs
3 recovery strategies: off-site power recovery, DG recovery, FW recovery
After loss of DGs, cooling is provided by RCIC/HPCI (mid figure); pressure control provided by SRV (left figure).
Torus pool temperature increases at each SRV activation (right figure).
When pool TH limits are reached, the RPV is depressurized; no cooling can be provided other than FW if available

## Slide 16: Workflow in RAVEN
Sample the RELAP5-3D model and create a database
Use generated data to seed the Adaptive Sampling Step
Compute failure probability from converged Solution

## Slide 17: Exercise 1: Create a data set to seed the Adaptive Sampler

## Slide 18: 1 – Sample a Model to seed the Adaptive Sampler
Samplers
Models
Distributions
Steps
Databases
DataObjects
<Distributions>
<Uniform name=’DGrecDist'>
<upperBound>28800</upperBound>
<lowerBound>0.0</lowerBound>
</Uniform>
<Uniform name=’DGrecDist'>
<upperBound>28800</upperBound>
<lowerBound>0.0</lowerBound>
</Uniform>
<!-- cont. 
</Distributions>
Lower and Upper bounds

## Slide 19: 1 – Sample a Model to seed the Adaptive Sampler
Models
Distributions
<Models>
<Code name=’MyRelap5' subType=’Relap5’>
<executable>path/to/relap5</executable>
<alias variable=”failureTemp”>0000503:1</alias>
</Code>
</Models>
Samplers
Steps
Databases
DataObjects
Executable location and name
Code Interface Type
Alias to have a more readable variable naming

## Slide 20: 1 – Sample a Model to seed the Adaptive Sampler
Samplers
Distributions
<Samplers>
<Stratified name=’LHS_Sampler'>
<variable name='0000200:1'>
<distribution>DGfailDist</distribution>
<grid type='CDF’ construction='equal' steps='4000’>0.0 1.0</grid>
</variable>
<variable name='0000579:6'>
<distribution>DGrecDist</distribution>
<grid type='CDF’ construction='equal' steps='4000’>0.0 1.0</grid>
</variable>
<!-- cont. -->
</Stratified>
</Samplers>
Models
Steps
Databases
DataObjects
<variable name>
<distribution>
<grid points>

## Slide 21: 1 – Sample a Model to seed the Adaptive Sampler
Distributions
<Databases>
<HDF5 name=’LHS_MC_database’ readMode=’overwrite'/>
</Databases>
<DataObjects>
<PointSet name=’FinalConditions'>
<Input>
0000582,0000583,0000597,0000596,0000200,
0000579,0000578,0000575,20508701,20508801,
failureTemp,0000588
</Input>
<Output>
timeof_692,timeof_578,timeof_591,timeof_672,cntrlvar_67,timeof_679
</Output>
</PointSet>
</DataObjects>
Databases
DataObjects
Samplers
Models
Steps
Overwrite or open in read mode?

## Slide 22: 1 – Sample a Model to seed the Adaptive Sampler
Distributions
Steps
Samplers
Models
Databases
DataObjects
Step
Model file
Model info
Sampler
Database
DataObjects
<Steps>
<MultiRun name='FirstMRun'>
<Input class=’Files' type=‘' >X11.i</Input>
<Input class=’Files' type=‘' >tpfh2o</Input>
<Model class='Models' type=’Code’ >MyRelap</Model>
<Sampler class='Samplers' type=’Stratified' >Grid_function</Sampler>
<Output class='DataObjects’ type=’PointSet’ >FinalConditions</Output>
<Output class='Databases' type='HDF5' >LHS_MC_database</Output>
</MultiRun>
</Steps>

## Slide 23: Exercise 2: Use generated data to seed the Adaptive Sampling Step and perform Limit Surface search

## Slide 24: 2- Use data to seed the Adaptive Sampling Step
<Models>
<Code name=’MyRelap5' subType=’Relap5’>
<executable>path/to/relap5</executable>
<alias variable=”failureTemp”>0000503:1</alias>
</Code>
<ROM name=’AccelerationROM' subType='SciKitLearn'>
<Features>
0000582,0000583,0000597,0000596,
0000200,0000579,0000578,0000575,
20508701,20508801,failureTemp,0000588
</Features>
<Target>goalFunction</Target>
<SKLtype>svm|SVC</SKLtype>
<kernel>rbf</kernel>
<C>10.0</C>
</ROM>
</Models>
Models
Steps
Databases
DataObjects
Functions
Samplers
Kernel Type
Penalty parameter of the error term

## Slide 25: 2- Use data to seed a Goal Oriented Sampling
<Functions>
<External name=’goalFunction’ file= ‘goalFunctionWorkshop’>
<variables>
failureTemp,cntrlvar_67
</variables>
</External>
</Functions>
Models
Steps
Databases
DataObjects
Functions
Samplers
Variables that are needed for the evaluation
Transition definition:
1 -> success
-1 -> failure
def __residuumSign(self):
if self.cntrlvar_67 >= self.failureTemp:
return -1
else:
return 1

## Slide 26: 2- Use data to seed the Adaptive Sampling Step
<Samplers>
<LimitSurfaceSearch name=’workshopAdaptive’>
<ROM class='Models' type='ROM’>accelerated_ROM</ROM>
<Function class='Functions' type='External’>goalFunction</Function>
<TargetEvaluation class='DataObjects' type=’PointSet'>
outAdaptive
</TargetEvaluation>
<Convergence
limit='3000'
forceIteration='False'
weight='value'
persistence='25'>
1e-4
</Convergence>
<variable name='0000200:1’><distribution>DGfailDist</distribution></variable>
<variable name='0000579:6’><distribution>DGrecDist</distribution></variable>
<!-- cont. -->
</LimitSurfaceSearch>
</Samplers>
Models
Steps
Databases
DataObjects
Functions
Samplers
Goal function
Max Iterations
Force Iteration until limit
Error Weighting: CDF or Value
Tolerance

## Slide 27: 2- Use data to seed a Goal Oriented Sampling
<Databases>
<HDF5 name='out_db_adaptive' directory=’DataBaseStorage/'/>
<HDF5 name=’LHS_MC_database’ readMode=’read’/>
</Databases>
<DataObjects>
<PointSet name='outAdaptive'>
<Input>
0000582,0000583,0000597,0000596,0000200,
0000579,0000578,0000575,20508701,20508801,
failureTemp,0000588
</Input>
<Output>
cntrlvar_67
</Output>
</PointSet >
<PointSet name=’limitSurface'>
<Input>0000582,0000583,0000597,0000596,0000200,0000579,0000578,
0000575,20508701,20508801,failureTemp,0000588</Input>
<Output>goalFunction</Output>
</PointSet >
</DataObjects>
Models
Steps
Databases
DataObjects
Functions
Samplers
Limit Surface Container

## Slide 28: 2- Use data to seed a Goal Oriented Sampling
<Steps>
<IOStep name=’load_seed_dataset'>
<Input class='Databases' type='HDF5' >LHS_MC_database</Input>
<Output class='DataObjects’ type='TimePointSet'>outAdaptive</Output>
</IOStep>
<MultiRun name=’GoalOrientedStep'>
<Input class=’Files' type=‘' >X11.i</Input>
<Input class=’Files' type=‘' >tpfh2o</Input>
<Model class='Models' type=’Code’ >MyRelap</Model>
<Sampler class='Samplers' type=’LimitSurfaceSearch’>workshopAdaptive</Sampler>
<Output class='DataObjects’type=’PointSet’ >outAdaptive</Output>
<Output class='Databases' type='HDF5' >out_db_adaptive</Output>
<SolutionExport class='DataObjects’type=’PointSet’>
limitSurface
</SolutionExport >
</MultiRun>
</Steps>
Models
Steps
Databases
DataObjects
Functions
Samplers

## Slide 29: Exercise 3: Compute failure probability from Converged solution

## Slide 30: 3 –Failure Probability from Converged Solution
Models
<Models>
<PostProcessor name=’limitSurfaceIntegral' subType=’LimitSurfaceIntegral’>
<integralType>MonteCarlo</integralType>
<seed>20021986</seed>
<target>goalFunction</target>
<variable name='0000200:1’><distribution>DGfailDist</distribution></variable>
<variable name='0000579:6’><distribution>DGrecDist</distribution></variable>
<!-- cont. -->
</PostProcessor >
</Models>
Steps
DataObjects
Feature space
Type of Integration

## Slide 31: 3 –Failure Probability from Converged Solution
<DataObjects>
<PointSet name=’limitSurface'>
<Input>
0000582,0000583,0000597,0000596,0000200,0000579,0000578,
0000575,20508701,20508801,failureTemp,0000588
</Input>
<Output>goalFunction</Output>
</PointSet >
</DataObjects>
Models
Steps
DataObjects
Previously generated Limit Surface

## Slide 32: 3 –Failure Probability from Converged Solution
<Steps>
<PostProcess name=’computeFailureProbability'>
<Input class='DataObjects' type=’PointSet' >limitSurface</Input>
<Model class=’Models’ type=’PostProcessor'>limitSurfaceIntegral</Output>
<Output class=’Files’ type=‘'>LimitSurfaceWeighted_out.csv</Output>
</PostProcess >
</Steps>
Models
Steps
DataObjects
Step
LimitSurface
OutputFile
Probability

## Slide 33: Thank you Questions?