## Slide 1: RAVEN interacting with external Applications
RAVEN Workshop
PSA 2015 - April 26th 2015, Sun Valley (ID)

## Slide 2: Outline
Brief introduction of RAVEN interacting with external Applications
  Available APIs: External Model and Code APIs
Using the External Model Entity:
  Introduction
  Implementing the Python Module
  Available Methods
  Interaction with RAVEN
Coupling a new Application through a Code Interface:
  Introduction
  Code requirements
  Interfaces that need to be implemented
  Interaction with RAVEN

## Slide 3: RAVEN interaction with external Applications
RAVEN owns two preferential APIs to interact with external Applications:
RAVEN
External Model
External Code
Both APIs are written in pure Python

## Slide 4: External Model

## Slide 5: Using the External Model entity: Introduction
The ExternalModel object represents an entity that is embedded in RAVEN at runtime.
This object allows the user to create a Python module that is going to be treated as a pre-defined internal Model.
RAVEN
External Model
imported
It becomes part of the RAVEN framework

## Slide 6: Using the External Model entity: RAVEN Input
<Models>
<ExternalModel name='PythonModule' subType=’’ ModuleToLoad='workshop_model’>
<variable>x1</variable>
<variable>y1</variable>
<newCustomXmlNode>
<printString>
We are not here
to brush the dolls
</printString>
</newCustomXmlNode>
</ExternalModel>
</Models>
File name
(with or without path): workshop_model.py
Model variables tracked by RAVEN
Variables that RAVEN is able to “see” and “check”
Custom piece of XML Input

## Slide 7: Using the External Model entity: Python module
In the External Python module, the user can implement all the methods that are needed for the functionality of the model, but only the following methods, if present, are called by the framework:
def _readMoreXML(self,xmlNode)
def initialize(self,runInfo,inputs)
def createNewInput(self,inputs,samplerType,**Kwargs)
def run(self,inputs)
Optional
Optional
Optional
Required
y1 = self.x1
Each variable defined in the XML input is available in “self”

## Slide 8: Using the External Model entity: _readMoreXML
def _readMoreXML(self,xmlNode):
# get the node
ourNode = xmlNode.find(’newCustomXmlNode’) # get the information in the node self.ourNewVariable = ourNode.text
<newCustomXmlNode> is unknown (in RAVEN)
The readMoreXML method can be implemented by the user if the XML input that belongs to this External Model needs to be extended to contain other information.
The information read needs to be stored in “self” in order to be available to all the other methods
Optional

## Slide 9: Using the External Model entity: initialize
def initialize(self,runInfo,inputs):
# initialize some quantities
self.sigma = 10.0 self.rho = 5.0
Variables not listed in the XML input files
The initialize method can be implemented in order to initialize the model.
For example, it can be used to compute a quantity needed by the “run” method:
Info read in <RunInfo> XML input
List of Inputs defined in the Step entity
Optional

## Slide 10: Using the External Model entity: createNewInput
def createNewInput(self,inputs,samplerType,**Kwargs):
if samplerType == ‘MonteCarlo’:
aVariable = inputs[‘anInput’]*self.sigma
else:
aVariable = inputs[‘anInput’]*self.rho
aLocalVar = Kwargs[‘SampledVars’][‘x1’]
returnVar = aVariable*aLocalVar
return returnVar
Type of Sampler
The createNewInput method might be used to create a custom Input with the information coming from RAVEN.
The generated input is going to be transferred to the “run” method.
Optional
Container of Info coming from RAVEN
From initialize method

## Slide 11: Using the External Model entity: run
def run(self,inputs):
input = inputs[0]
self.y1 = returnVar**2
return
In this function, the user needs to implement the algorithm that RAVEN will execute.
The run method is generally called after having inquired the createNewInput method (internal or the user-implemented)
Optional
Required
List of Inputs generated in creatNewInput method
Outcome stored in “self” => RAVEN can collect it

## Slide 12: Code Interface

## Slide 13: Coupling an Application with RAVEN: Introduction
The procedure of coupling a new Application with RAVEN is a straightforward process.
The coupling is performed through a Python Interface that is in charge of interpreting the information coming from RAVEN and translating them in the input of the system code under consideration.
The coupling procedure does not require to modify RAVEN itself.
RAVEN
External Code
embedded
Interpreting information coming from RAVEN
Translating them in the Application Input

## Slide 14: Coupling an Application with RAVEN: Requirements
Input requirements:
  Python-compatible parser for Application input:
  Decide the syntax your Code Interface will be able to interpret
class simpleInputParser():
def __init__(self,filen):
self.keyDict = {} lines=open(filen).readlines() for line in lines:
key=line.split("=”)[0] value=line.split("=”)[1]
self.keyDict[key]=value
def modifyInternalDict(self,inDictionary):
for key,newvalue in inDictionary.items():
self.keyDict[key]=newvalue
def writeNewInput(self,filen):
fileobject = open(filen)
for key,value in self.keyDict.items():
fileobject.write(key+‘‘=’’+str(value)+‘‘\n’’)
Input Parser Example
Key1 = aValue1
Key2 = aValue2
Key3 = aValue3
Input Text

## Slide 15: Coupling an Application with RAVEN: Requirements
  Output requirements:
    RAVEN handles Comma Separated Values (CSV) files
  If your code output is not in CSV format, your interface needs to be able to convert it into CSV format
def convertOutputFileToCSV(outfile):
keywordDict = {} fileobject = open(outputfile)
outputCSVfile = open (outputfile + ’.csv’)
lines = fileobject.readlines()
for line in lines:
listSplitted = line.split("=")
keyword = listSplitted[0] value = listSplitted[1]
keyDict[keyword] = value
outputCSVfile.write(’,’.join(keyDict.keys()))
outputCSVfile.write(’,’.join(keyDict.values()))
Input Parser Example
result1= aValue1
result2= aValue2
Output Text
result1,result2
aValue1,aValue2
Output CSV

## Slide 16: Coupling an Application with RAVEN: Interfaces
RAVEN becomes aware of the codes it can use as Models only at run-time, since it looks for code interfaces and loads them automatically
The code interface needs to be placed in a new folder under the directory “./raven/framework/CodeInterfaces”

## Slide 17: Coupling an Application with RAVEN: Methods
def generateCommand(self,input,exe,clargs,fargs)
def finalizeCodeOutput(self,command,output,workDir)
def createNewInput(self,inputs,samplerType,**Kwargs)
def getInputExtension(self)
Optional
Optional
Required
class newApplication(CodeInterfaceBase):
RAVEN imports all the “Code Interfaces” at run-time, without actually knowing the syntax of the driven codes.
In order to make RAVEN able to drive a new Application, a Python module containing few methods (strict syntax) needs to be implemented:
def checkForOutputFailure(self,output,workDir)
Optional
Required

## Slide 18: Coupling an Application with RAVEN: generateCommand
def generateCommand(self,input,exe,clargs,fargs):
inp = input[0]
outfile=’out ̃’+os.path.split(inp)[1].split(’.’)[0]
executeCommand = (exe+ ‘ -i ‘ +os.path.split(inp)[1])
return (executeCommand,outfile)
The generateCommand method is used to retrieve the command needed to launch the driven App and the root of the output file.
The return data type must be a TUPLE.
Optional
Required
List of input files
Executable
Optional Arguments

## Slide 19: Coupling an Application with RAVEN: createNewInput
Optional
The createNewInput method is used to generate an input based on the information RAVEN passes in.
This method needs to return a list containing the path and filenames of the modified input files.
Optional
Required
def createNewInput(self,inputs,samplerType,**Kwargs):
parser = simpleInputParser(currentInputFiles[0])
sampledVars = Kwargs[’SampledVars’]
parser.modifyInternalDictionary(sampledVars)
temp = str(inputs[index][:])
newInputFiles = copy.copy(inputs)
newInputFiles[0] = os.path.join(os.path.split(temp)
[0], Kwargs[’prefix’]+" ̃"+os.path.split(temp)[1])
parser.writeNewInput(newInputFiles[0]) return newInputFiles
Type of Sampler
List of inputs
Dictionary of info from RAVEN
Notes: It needs to modify the input file, accordingly with respect to the variables RAVEN is providing.

## Slide 20: Coupling an Application with RAVEN: finalizeCodeOutput
Optional
The finalizeCodeOutput can be used to convert the whatever App output format into a CSV.
RAVEN checks if a string is returned; if so, RAVEN interprets that string as the new output file name (CSV).
Optional
def finalizeCodeOutput(self,command,output,workDir):
outputfile = os.path.join(workingDir,output+’.o’)
convertOutputFileToCSV(outfile)
Command created by generateCommand
Output root name
Working directory
Notes: It needs to modify the input file, accordingly with respect to the variables RAVEN is providing.

## Slide 21: Appendix: Python

## Slide 22: Brief introduction to Python: why Python?
Natural Language Tool-Kit
Ease of use => interpreter
AI Processing: Symbolic
  Python’s built-in datatypes for strings, lists, and more.
  Java or C++ require the use of special classes for this.
AI Processing: Statistical
  Python has strong numeric processing capabilities: matrix operations, etc.
  Suitable for probability and machine learning code.

## Slide 23: Brief introduction to Python: Example
x = 34 - 23 # A comment.
y = “Hello” # Another one.
z = 3.45
if z == 3.45 or y == “Hello”:
x = x + 1
y = y + “ World” # String concat.
print x
print y

## Slide 24: Brief introduction to Python: Basic knowledge
Assignment uses = and comparison uses ==.
For numbers +-*/% are as expected.
  Special use of + for string concatenation.
  Special use of % for string formatting.
Logical operators are words (and, or, not) not symbols (&&, ||, !).
The basic printing command is “print.”
First assignment to a variable will create it.
  Variable types don’t need to be declared.
  Python figures out the variable types on its own.

## Slide 25: Brief introduction to Python: datatypes
Integers (default for numbers)
  z = 5 / 2 # Answer is 2, integer division.
Floats
  x = 3.456
Strings
  Can use “” or ‘’ to specify. “abc” ‘abc’ (Same thing.)
  Unmatched ones can occur within the string. “matt’s”
  Use triple double-quotes for multi-line strings or strings than contain both ‘ and “ inside of them: “““a‘b“c”””
Lists
  Lists are unsorted array of objects (floats, integers, derived types, etc.)
  a = [“Hello”,5.0,1]
Dictionaries
  Dictionaries are objects that employ a mapping between string keys and objects
  a = {‘a’:1.0,’b’:’Hello’,’c’:1}

## Slide 26
Whitespace is meaningful in Python: especially indentation and placement of newlines.
  Use a newline to end a line of code. (Not a semicolon like in C++ or Java.) (Use \ when must go to next line prematurely.)
  No braces { } to mark blocks of code in Python… Use consistent indentation instead. The first line with a new indentation is considered outside of the block.
  Often a colon appears at the start of a new block. (We’ll see this later for function and class definitions.)
Brief introduction to Python: whitespace

## Slide 27
Start comments with # – the rest of line is ignored.
Can include a “documentation string” as the first line of any new function or class that you define.
The development environment, debugger, and other tools use it: it’s good style to include one.
  def my_function(x, y):
  “““This is the docstring. This function does blah blah blah.””” # The code would go here...
Brief introduction to Python: Comments

## Slide 28: Brief introduction to Python: example
x = 34 - 23 # A comment.
y = “Hello” # Another one.
z = 3.45
if z == 3.45 or y == “Hello”:
x = x + 1
y = y + “ World” # String concat.
print x
print y

## Slide 29
Python determines the data types in a program automatically. “Dynamic Typing”
But Python’s not casual about types, it enforces them after it figures them out. “Strong Typing”
So, for example, you can’t just append an integer to a string. You must first convert the integer to a string itself.
x = “the answer is ” # Decides x is string.
y = 23 # Decides y is integer.
print x + y # Python will complain about this.
Brief introduction to Python: Python and Types

## Slide 30: Brief introduction to Python: Naming Rules
Names are case sensitive and cannot start with a number. They can contain letters, numbers, and underscores.
  bob Bob _bob _2_bob_ bob_2 BoB
There are some reserved words:
  and, assert, break, class, continue, def, del, elif, else, except, exec, finally, for, from, global, if, import, in, is, lambda, not, or, pass, print, raise, return, try, while