## Slide 1: Reduced Order Models (ROMs) and RAVEN
RAVEN Workshop
IRUG 2016
Presenter: Andrea Alfonsi

## Slide 2: Outline
Brief introduction on ROMs
Application examples of ROMs
ROMs and RAVEN
  Available ROMs
  RAVEN ROM workflow
Ensemble Modeling
RAVEN examples
  Create ROMs
  Perform sampling of ROMs
  Statistical Analysis

## Slide 3: ROMs: a Quick Introduction
Consider a set of N data points
Build a surrogate model
  Reduced Order Model
Inputs: Initial and boundary conditions
Output: Simulation outcome (success/failure, max clad temperature)
≅
DataObjects
(PointSet)

## Slide 4: ROMs: a Quick Introduction
Basically we are trying to reduce the complexity of the original model
Pros:
  Much faster computation of the output variables
Cons:
  Possible presence of error in the ROM computed values
≅
Original data (e.g., RELAP5)
ROM (e.g., quadratic regressor)

## Slide 5: ROMs: Applications
Basic steps:
  Sample original model
  Train the ROM
  Perform desired analysis with the ROM
  instead of the original model
Range of applications:
  Uncertainty quantification / Sensitivity analysis
  Probabilistic Risk Analysis (PRA)
  Accelerator for stochastic analysis (adaptive sampling)
  Prediction models
Input x
Output y

## Slide 6: ROMs Available in RAVEN
  External libraries: Scikit-learn (http://scikit-learn.org)
  Classification
  Regression
  Data clustering
  Dimensionality reduction
  Data pre-processing
Internally C++ developed libraries: CROW
  Generalized Polynomial Chaos
  Multi-dimensional interpolators
    ND Spline
    ND Inverse-Weight

## Slide 7: Scikit-Learn Library
Classification
  Starting point: set of data points with labels
  [features, class]i
  Objective: identify which class a new point [features] belong
Regression
  Objective: estimate the relationships among variables via a statistical process
  Outcome: coefficients of the reduced space (e.g., m and c for linear interpolator)
Notes: Add backup slides for some algorithms GPM and SVM

## Slide 8: Cross-Validation for assessing ROM validity
Take out some of the training set
  Train on the remaining training set
  Test on the excluded instances
  Cross-validation
k-fold cross-validation
Train
Test
Dataset
Compute a score (e.g. R2)

## Slide 9: Ensemble Modeling Motivations
In several cases multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others
In order to face this “problem” in the RAVEN framework, a new model category (e.g. class), named EnsambleModel, has been designed
This class is able to assemble multiple models of other categories (i.e. Code, External Model, ROM), identifying:
  the input/output connections
  the order of execution
  the parallel execution strategy for each sub-model
EnsembleModel
Physics 1
Physics 2

## Slide 10: Ensemble Model
Assemble multiple models of other categories, identifying the input/output connections and the order of execution
Common information transfer interface (RAVEN Data Objects)
Able to propagate both scalar and 1-Dimensional (e.g. time-series) info
Notes: Sometimes, multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others

## Slide 11
Model 1
Model 2
Model 3
Model 1
Model 2
Model 3
3 sub-models:
  The Model 2 is connected with the Model 1 through the variable Θ (Model 1 output and Model 2 input)
  The Model 3 is connected with the Model 2 through the variable Π (Model 2 output and Model 3 input)
Serial sequence
Multiple parallel execution
Ensemble Model: Chain of Models
Notes: Sometimes, multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others.
Parallel execution, chain execution

## Slide 12: RAVEN ensemble modeling example

## Slide 13
Hypothetical simplified PWR model:
  EM1, A pump controller model for a hypothetical simplified PWR model has been used. It consists of Reactor core (RX), Motor operated pump, Pump digital controller and Heat exchanger (HX). This system is responsible to remove the decay heat generated from the core (RX) in order to avoid damage of the core itself.
  EM2, A power history generator model has been used. It employs of the following simple equation:
Power(t) = 1,500*scalingP*exp⁡(-t)
Ensemble Model Time-dependent example

## Slide 14: Ensemble Model Time-dependent example
Stochastic Parameters:
  Pump controller failure time (CNTRf,time):
    Exponential Distribution, λ=0.00138889
  Pump controller failure mode (CNTRf,mode):
    Categorical (0.33 each bin):
      Mode 1: Failed Closed
      Mode 2: Failed Stuck
      Mode 3: Failed Random
  Power multiplier (scalingP):
    Uniform between 0.5 and 1.5

## Slide 15: Ensemble Model Time-dependent example
Power(t)
Temperature(t)
Outcome
1500 Monte-Carlo samples
Most of the failures occur when the controller failed by sanding close signal to the pump
Notes: 1500 Monte-Carlo simulations
Most of the failures happened in failure mode 1 (i.e. controller failed by sending close signal to pump (i.e., pump not running)

## Slide 16: ROM and Ensemble Modeling Within RAVEN
All modeling steps that involve ROMs are available in RAVEN
  Create ROMs from a database
  Perform statistical analysis using ROMs
  Ensemble modeling

## Slide 17: BWR SBO Scenario: Overview
Plant considered: BWR with Mk.I containment
Test case: Loss of Offsite Power (LOOP) + Loss of Diesel Generators
Objectives:
  Evaluate impact of power uprate on LOOP+SBO accident scenario
  Show capabilities of simulation based Probabilistic Risk Assessment (PRA) through RISMC

## Slide 18: BWR SBO Scenario: Overview
Systems considered
  Reactor Pressure Vessel (RPV) level control:
    Reactor Core Isolation Cooling System (RCIC)
    High Core Injection (HPCI)
  RPV pressure control:
    Safety Relief Valves (SRVs) including ADS
  Containment:
    Drywell (DW)
    Suppression Pool (SP)
  Reactor pump seal
  Firewater injection system
  Operators
  Power Systems
    Battery systems (DC systems)
    Normal and emergency AC Power systems:
      Power-grid
      DGs

## Slide 19: BWR SBO Scenario: Scenario Example
LOOP
Reactor trips
Main Steam Isolation Valves close
DGs successfully start
DC power and associated buses are available
AC recovery
Firewater Injection
RPV
depressurization
RHR activation
DC power
extinguished
Loss of DGs: SBO condition
  RPV Pressure control: SRV
  RPV Level control : RCIC (or HPCI)
  Containment control (drywell and suppression pool)
Seal LOCA
Notes: Scenario: LOOP + loss of DGs
Initial event: LOOP with successful reactor trip
DG failure occurs randomly after that
At this point (SBO conditions), operators maintain pressure and level control in RPV and suppression pool until limits are reached
cooling is provided by RCIC/HPCI (mid figure); pressure control provided by SRV (left figure).
Due to loss of cooling, pump seals may deteriorate leading to leaks in the drywell and thus reaching RPV depressurization point more quickly
3 recovery strategies: off-site power recovery, DG recovery, FW activation
After loss of DGs, Torus pool temperature increases at each SRV activation (right figure).
When pool TH limits are reached, the RPV is depressurized; no cooling can be provided other than FW if available
When RPV is depressurized, FW can be considered a recovery action even though it would compromise plant

## Slide 20: BWR SBO Scenario: Stochastic Parameters
Stochastic parameters
  Failure time of DGs
  Recovery time of DGs
  Battery life
  SRVs fails open time
  Offsite AC power recovery
  Clad Fail temperature
  HPCI fails to run
  RCIC fails to run
  Firewater availability time
  Extended ECCS operation
  Manual ADS activation

## Slide 21: Workflow
Sample RELAP5 model Create database
Train a ROM
Sample ROM
Statistical Analysis

## Slide 22
Sample RELAP5 model Create database
Train a ROM
Sample ROM
Statistical Analysis

## Slide 23: 1 – Sample a Model to create a database
Samplers
Models
Distributions
Steps
Databases
DataObjects
<Distributions>
<Uniform name=’DGrecDist'>
<upperBound>28800</upperBound>
<lowerBound>0.0</lowerBound>
</Uniform>
<Uniform name=’DGrecDist'>
<upperBound>28800</upperBound>
<lowerBound>0.0</lowerBound>
</Uniform>
<!-- cont. 
</Distributions>
Lower and Upper bounds

## Slide 24: 1 – Sample a Model to create a database
Models
Distributions
<Models>
<Code name=’MyRelap5' subType=’Relap5’>
<executable>path/to/relap5</executable>
<alias variable=”failureTemp”>0000503:1</alias>
</Code>
</Models>
Samplers
Steps
Databases
DataObjects
Executable location and name
Code Interface Type
Alias to have a more readable variable naming

## Slide 25: 1 – Sample a Model to create a database
Samplers
Distributions
<Samplers>
<Stratified name=’LHS_Sampler'>
<variable name='0000200:1'>
<distribution>DGfailDist</distribution>
<grid type='CDF’ construction='equal' steps='4000’>0.0 1.0</grid>
</variable>
<variable name='0000579:6'>
<distribution>DGrecDist</distribution>
<grid type='CDF’ construction='equal' steps='4000’>0.0 1.0</grid>
</variable>
<!-- cont. -->
</Stratified>
</Samplers>
Models
Steps
Databases
DataObjects
<variable name>
<distribution>
<grid points>

## Slide 26: 1 – Sample a Model to create a database
Distributions
<Databases>
<HDF5 name=’LHS_MC_database’ readMode=’overwrite'/>
</Databases>
<DataObjects>
<PointSet name=’FinalConditions'>
<Input>
0000582,0000583,0000597,0000596,0000200,
0000579,0000578,0000575,20508701,20508801,
failureTemp,0000588
</Input>
<Output>
timeof_692,timeof_578,timeof_591,timeof_672,cntrlvar_67,timeof_679
</Output>
</PointSet>
</DataObjects>
Databases
DataObjects
Samplers
Models
Steps
Overwrite or open in read mode?

## Slide 27: 1 – Sample a Model to create a database
Distributions
Steps
Samplers
Models
Databases
DataObjects
Step
Model file
Model info
Sampler
Database
DataObjects
<Steps>
<MultiRun name='FirstMRun'>
<Input class=’Files' type=‘' >X11.i</Input>
<Input class=’Files' type=‘' >tpfh2o</Input>
<Model class='Models' type=’Code’ >MyRelap</Model>
<Sampler class='Samplers' type=’Stratified' >Grid_function</Sampler>
<Output class='DataObjects’ type=’PointSet’ >FinalConditions</Output>
<Output class='Databases' type='HDF5' >LHS_MC_database</Output>
</MultiRun>
</Steps>

## Slide 28: Workflow
Sample RELAP5 model Create database
Train a ROM
Sample ROM
Statistical Analysis

## Slide 29: 2 – Train, Sample and perform SA on a ROM
<Distributions>
<Uniform name=’DGrecDist'>
<upperBound>28800</upperBound>
<lowerBound>0.0</lowerBound>
</Uniform>
<Uniform name=’DGrecDist'>
<upperBound>28800</upperBound>
<lowerBound>0.0</lowerBound>
</Uniform>
<!-- cont. 
</Distributions>
Samplers
Models
Distributions
Steps
Databases
DataObjects
Lower and Upper bounds

## Slide 30: 2 – Train, Sample and perform SA on a ROM
Models
Distributions
Samplers
Steps
Databases
DataObjects
<Models>
<ROM name=’SurrogateRELAP5' subType=’NDinvDistWeight'>
<Target>cntrlvar_67</Target>
<Features>
0000582,0000583,0000597,0000596,
0000200,0000579,0000578,0000575,
20508701,20508801,failureTemp,0000588
</Features>
<p>3</p>
</ROM>
<PostProcessor name=’stas' subType=’BasicStatistics’>
<what>all</what>
<parameters>
cntrlvar_67, 0000582,0000583,0000597,0000596,
0000200,0000579,0000578,0000575,
20508701,20508801,failureTemp,0000588
</parameters>
</PostProcessor >
</Models>
Coefficient
Multi-dimensional interpolator (CROW)
Which Statistical FOMs?
Which Parameters?

## Slide 31: 2 – Train, Sample and perform SA on a ROM
Samplers
Distributions
Models
Steps
Databases
DataObjects
<Samplers>
<Stratified name=’LHS_SamplerROM'>
<variable name='0000200:1'>
<distribution>DGfailDist</distribution>
<grid type='CDF’ construction='equal' steps=‘8000’>0.0 1.0</grid>
</variable>
<variable name='0000579:6'>
<distribution>DGrecDist</distribution>
<grid type='CDF’ construction='equal' steps=‘8000’>0.0 1.0</grid>
</variable>
<!-- cont. -->
</Stratified>
</Samplers>
Finer Grid:
8000 vs. 4000

## Slide 32: 2 – Train, Sample and perform SA on a ROM
Distributions
Databases
DataObjects
Samplers
Models
Steps
<Databases>
<HDF5 name=’LHS_MC_database’ readMode=’read’/>
</Databases>
<DataObjects>
<PointSet name=’trainingData'>
<Input>
0000582,0000583,0000597,0000596,0000200,
0000579,0000578,0000575,20508701,20508801,
failureTemp,0000588
</Input>
<Output>
cntrlvar_67
</Output>
</PointSet >
<PointSet name=’outputROM'>
<Input>0000582,0000583,0000597,0000596,0000200,0000579,0000578,
0000575,20508701,20508801,failureTemp,0000588</Input>
<Output>cntrlvar_67</Output>
</PointSet >
</DataObjects>
Database containing training set
Training DataObject
ROM generated DataObject

## Slide 33: 2 – Train, Sample and perform SA on a ROM
Distributions
<Steps>
<IOStep name='extract_data'>
<Input class='Databases' type='HDF5' >LHS_MC_Database</Input>
<Output class='DataObjects' type=’PointSet’ >trainingData</Output>
</IOStep>
<RomTrainer name='rom_trainer'>
<Input class='DataObjects' type=’PointSet’ >trainingData</Input>
<Output class='Models' type='ROM' >SurrogateRELAP5</Output>
</RomTrainer>
<MultiRun name=’RunRom4'>
<Input class='DataObjects’ type=’PointSet’ >Data</Input>
<Model class='Models' type=’ROM’ >SurrogateRELAP5</Model>
<Sampler class='Samplers' type=’Stratified' >LHS_SamplerROM</Sampler>
<Output class='DataObjects’ type='PointSet' >outputROM</Output>
</MultiRun>
<PostProcess name=’statistics'>
<Input class='DataObjects’ type=’PointSet’ >outputROM</Input>
<Model class='Models' type=’PostProcess’ >stats</Model>
<Output class=’Files’ type=‘' >outputROM_stats.csv</Output>
</MultiRun>
</Steps>
Steps
Samplers
Models
Databases
DataObjects

## Slide 34: 2 – Train, Sample and perform SA on a ROM
Computed Quantities | ROM | RELAP5-3D
Percentile 5% | 1.84E+03 | 1.84E+03
Percentile 95% | 2.56E+03 | 2.56E+03
Median | 2.20E+03 | 2.20E+03
Expected Value | 2.20E+03 | 2.20E+03
Variance | 5.33E+04 | 5.33E+04
Sigma | 2.31E+02 | 2.31E+02
Skewness | -2.38E-06 | -2.20E-06

## Slide 35: 3 – Ensemble modeling
Models
<Models>
<ROM name=’ROM1' subType='NDinvDistWeight'>
<Features>x1,x2</Features>
<Target>y1</Target>
</ROM>
<ROM name=’ROM2' subType='NDinvDistWeight'>
<Features>x1,x2,y1</Features>
<Target>y2</Target>
</ROM>
<EnsembleModel name=’together' subType=‘'>
<Model class='Models’ type=’ROM’>ROM1
<TargetEvaluation class=’DataObjects’type=’PointSet’>
ROM1Output
</TargetEvaluation>
</Model>
<Model class='Models’ type=’ROM’>ROM2
<TargetEvaluation class=’DataObjects’type=’PointSet’>
ROM2Output
</TargetEvaluation>
</Model>
</EnsembleModel>
</Models>
Steps
DataObjects
y1 is in:
ROM1 output space
ROM2 input space
This DataObjects define the in/out relations

## Slide 36: 3 – Ensemble modeling
<DataObjects>
<PointSet name=’ outputROM1'>
<Input>x1,x2</Input>
<Output>y1</Output>
</PointSet >
<PointSet name=’outputROM2'>
<Input>x1,x2,y1</Input>
<Output>y2</Output>
</PointSet >
<PointSet name=’fullOutput'>
<Input>x1,x2</Input>
<Output>y2,y1</Output>
</PointSet >
</DataObjects>
Full Output
Models
Steps
DataObjects

## Slide 37: 3 – Ensemble modeling
<Steps>
<MultiRun name=’sampleEnsemble'>
<Input class='DataObjects’ type=’PointSet’ >Data</Input>
<Model class='Models' type=’EnsembleModel’>together</Model>
<Sampler class='Samplers' type=’Stratified' >LHS_SamplerEnsemb</Sampler>
<Output class='DataObjects’ type='PointSet' >fullOutput</Output>
</MultiRun>
</Steps>
Models
Steps
DataObjects
Sample the EnsembleModel

## Slide 38: Thank you Questions?